## Slide 1
ELECTRONICS WORKSHOP PROJECT
Gesture-Controlled Music Player
using Visible Light Communication (VLC)
TEAM: CHAMMAKS
• Shreyaas Sarkar
• Jonathan Robin
• Aditya Gokhale
DEPARTMENT / INSTITUTION
Electronics & Communication Engineering
Academic Year: 2025 – 2026

## Slide 2
ELECTRONICS WORKSHOP (EW) PROJECT
Problem Statement & Project Interpretation
The Engineering Challenge
• Traditional wireless controllers rely exclusively on RF (Bluetooth/Wi-Fi), introducing RF congestion, radiation, and security vulnerabilities.
• Conventional audio playback requires physical touch or line-of-sight buttons, impractical in sterile or active workshop environments.
• Objective: Design and fabricate an optical, contactless human-machine interface combining gesture kinematics with optical wireless communication.
Our System Interpretation
• Wearable Sensing Subsystem: Glove mounted with 2x analog flex sensors and MPU-6050 6-DOF IMU detects hand orientation and finger bends.
• Optical Wireless Channel: Converts recognized gesture commands into high-speed modulated visible light pulses (450 nm – 650 nm).
• Audio Base Station: Fast photodiode detects light signals, validates checksums, actuates servo directional aiming, and drives dual I2S speakers.

## Slide 3
ELECTRONICS WORKSHOP (EW) PROJECT
System Overview & Workflow Architecture
1. Wearable Glove Unit
• MPU-6050: Samples pitch and roll angles at 50 Hz via I2C bus.
• Flex Sensors: Voltage divider network measures finger curling.
• Sensor Fusion: Complementary filter eliminates drift & hand tremors.
• Frame Assembly: Generates 6-byte packet with sync preamble & XOR CRC.
2. Optical VLC Channel
• Visible Emitter: High-brightness LED (Blue 465 nm or focused Red 650 nm).
• Modulation: 2400-baud UART-over-light or 50 kHz high-speed audio PWM.
• Physical Security: Confined within room boundaries (cannot pass walls).
• Zero RF EMI: Completely safe for sensitive lab and medical environments.
3. Audio Base Station
• Optical RX: Fast PIN photodiode + LM393 comparator pulse recovery.
• Actuation: SG90 micro-servo rotates optical receiver/speaker aim.
• Dual I2S Audio: Shared BCLK/LRC/DIN to two MAX98357A Class-D DACs.
• Output: Independent channel shutdown powers stereo 3W speakers.

## Slide 4
ELECTRONICS WORKSHOP (EW) PROJECT
Hardware Components & Specifications
Component Name | Qty | Technical Specifications / Purpose | Role in System
ESP32-WROOM-32 Dev Kit | 2–3 | Dual Tensilica Xtensa @ 240 MHz, Hardware I2S, I2C, ADC, BLE | Processing brains (Glove & Base)
MPU-6050 6-DOF IMU | 1 | 3-axis Accelerometer + 3-axis Gyroscope, I2C fast mode (0x68) | Hand tilt & motion capture
Analog Flex Sensors (2.2") | 2 | Variable resistive strip (~10kΩ flat, ~35kΩ bent 90°) | Index & middle finger bend sensing
Visible Light LED Emitter | 1–2 | High-flux 5mm LED (Blue 465nm / Red 650nm) + 2N2222 Driver | Optical VLC transmitter
PIN Photodiode Module | 1–2 | Visible-spectrum photodiode with LM393 analog comparator | Optical signal receiver
MAX98357A I2S Class-D Amp | 2 | 3.2W into 4Ω, hardware I2S PCM input, independent SD pin | Digital audio DAC & amplification
SG90 Micro Servo + 3W Spks | 1 + 2 | 50 Hz PWM position control (0°–180°), 4Ω dynamic speakers | Directional steering & sound output

## Slide 5
ELECTRONICS WORKSHOP (EW) PROJECT
Kinematic Gesture Recognition Matrix
Hand Gesture | Sensor Threshold Criteria | VLC Opcode | Assigned Action / Function
Fist Clench | Flex 1 < 1850 AND Flex 2 < 1850 (both curled) | 0x10 | Play / Pause Audio Toggle
Tilt Forward | Pitch < -28° (fingers extended) | 0x21 | Volume Down (–5% step)
Tilt Backward | Pitch > +28° (fingers extended) | 0x20 | Volume Up (+5% step)
Tilt Left | Roll < -32° (hand tilted counter-clockwise) | 0x31 | Previous Track (or Prev Slide)
Tilt Right | Roll > +32° (hand tilted clockwise) | 0x30 | Next Track (or Next Slide)
Index Point | Flex 1 straight (>2300), Flex 2 bent (<1850) | 0x40 | Route Audio to Speaker A (Left)
Peace Sign (V) | Flex 1 straight (>2300), Flex 2 straight (>2300) | 0x41 | Route Audio to Speaker B (Right)

## Slide 6
ELECTRONICS WORKSHOP (EW) PROJECT
Circuit Representation & Hardware Pinouts
Transmitter Glove Interfacing
• MPU-6050 I2C Bus: SDA -> GPIO 21, SCL -> GPIO 22 (Fast Mode 400 kHz).
• Index Flex Sensor: GPIO 34 (ADC1_CH6) with 22 kΩ precision pull-down.
• Middle Flex Sensor: GPIO 35 (ADC1_CH7) with 22 kΩ precision pull-down.
• VLC Driver: GPIO 17 -> 1 kΩ base resistor -> 2N2222 NPN transistor driving 5mm high-flux LED.
• Portable Power: 3.7V 1000 mAh LiPo battery through TP4056 charge/protection board.
Base Station & Audio Interfacing
• Optical Receiver: Photodiode digital out (DO) -> GPIO 4 (UART RX pulse).
• Shared I2S Audio Bus: BCLK -> GPIO 22, LRC/WS -> GPIO 21, DIN -> GPIO 19.
• Amplifier Enables: Amp 1 SD_MODE -> GPIO 25, Amp 2 SD_MODE -> GPIO 26.
• Actuator Control: SG90 Micro Servo Signal -> GPIO 18 (LEDC 50 Hz PWM).
• Brownout Protection: 100 µF electrolytic decoupling cap across 5V motor/audio rail.

## Slide 7
ELECTRONICS WORKSHOP (EW) PROJECT
Mid-Evaluation Status & Milestone Roadmap
Completed Milestones (Mid-Eval)
• ✅ Sensor Calibration: Interfaced MPU-6050 & flex sensors with ESP32; established noise-immune threshold boundaries.
• ✅ Complementary Filtering: Stable pitch/roll tracking without gimbal drift or high-frequency vibration jitter.
• ✅ Optical Communication: Validated high-frequency LED pulsing and photodiode demodulation over line-of-sight.
• ✅ Dual-Mode Controller: Implemented both direct optical framing and BLE HID media/presentation navigation.
Final Evaluation Roadmap (Pending)
• ⏳ Spatial Audio Steering: Calibrate SG90 micro-servo mapping to dynamically steer optical transmitter beam.
• ⏳ Dual-Speaker Switching: Integrate independent SD_MODE line toggling to seamlessly transfer audio between speakers.
• ⏳ Optical Collimation Enclosure: 3D-print narrow-beam lens shrouds to enhance daylight ambient noise rejection.
• ⏳ Final Project Showcase: Conduct live demonstration of hands-free music and slide presentation control.

## Slide 8
ELECTRONICS WORKSHOP (EW) PROJECT
Summary, Deliverables & Acknowledgments
Project Summary & Takeaways
• Successful Proof of Concept: Proves the viability of Visible Light Communication for contactless human-machine interaction.
• RF-Free Architecture: Achieves wireless digital audio and media command transmission without electromagnetic interference.
• Embedded Optimization: Utilizes FreeRTOS dual-core task scheduling to guarantee zero-jitter audio playback alongside optical decoding.
Team Chammaks & Responsibilities
• Shreyaas Sarkar
Role: Sensor glove fabrication, kinematics calibration, wearable assembly
• Jonathan Robin
Role: VLC optical transmitter driver, photodiode amplifier, audio DSP
• Aditya Gokhale
Role: FreeRTOS firmware, I2S bus integration, hardware testing & slides
Course Faculty & Acknowledgments
Sincere gratitude to the Electronics Workshop Course Coordinator, Lab Instructors, and Department Technical Staff for continuous guidance and laboratory support.